## Slide 1: Excavators
Lecture 7
TSP-308 MPK Ferdinand Fassa

## Slide 2: OUTLINE
Introduction
Type of Excavator

## Slide 3: INTRODUCTION
Hydraulic front shovel are used for hard digging above track level and for loading haul units
Hydraulic hoe excavator are used to excavated below natural surface of the ground on

## Slide 4: Type of Excavators
Backhoes
Clamshells
Draglines
Trenchers
Front Shovels (Power Shovels)

## Slide 5: Excavators
excavate and load dirt (soil/aggregate) to haulers

## Slide 6: Anatomy of Excavator

## Slide 7: Draglines

## Slide 8: Under Carriage
Crawler-Mounted
Wheel-Mounted
Truck-Mounted

## Slide 9: Factors Affecting Excavators’ Productivity
Types and characteristics of soils
Depth of Cut
Angle of Swing
Types and sizes of buckets
Length of boom
Efficiency and condition of equipment
Efficiency and condition of work

## Slide 10: Loading Mechanism

## Slide 11: Excavator Productivity
Bucket Capacity (manufacture listed specs)
    volume (heaped / struck)
    weight (static tipping load, front or side, outriggers)
Bucket Fill Factors (type of material)
Cycle Time
    Load-raise, swing, dump, swing back, lower,
Correction Factors
    Bucket Fill factor
    % Optimum Depth of Cut – Angle of Swing
    working and management conditions
P = corrected bucket capacity / cycle time

## Slide 12: Buckets

## Slide 13: Tables for Backhoe

## Slide 14: Correction factor for Opt. Depth of Cut – Angle of Swing

## Slide 15: exercise
Determine actual productivity of a backhoe loader having
optimum dept of cut of 2.2 m and working to excavate sand at depth of 2.5 m and angle of swing 150o. Bucket size is 3 cy.
Percent swell 26%
Working in 40 min-hour.
Total cycle time = 20 sec
bucket fill factor 95%
bucket load = 95% * 3 cy = 2.85 Lcy
% opt. depth of cut = dept of excavation/ max dept
= 2.5 m/2.2 m
=114%
Correction factor:
= 1/(1+ swell factor)
= 1/(1+0.26)  0.79
Estimated productivity:
= (bucket size x fill factor x working efficiency) cycle time
(2.85 Lcy x 0.79 x 40/60) / 20 = 0.075 lcy/s x 3600 s
    = 270 Lcy/hr

## Slide 16
CONSTRUCTION EQUIPMENT AND METHODS
Next
Lecture 8