## Slide 1: Robotics System Lecture 11_12: DC Motor
By:
Nur Uddin, Ph.D

## Slide 2: Motor Basics

## Slide 3: An inductor with resistance

## Slide 4: Remember this Waveform!
Note how the current levels off.
This will provide a steady speed.

## Slide 5: H-Bridge Basics
control the speed and direction of a motor
use Power Electronics… MOSFET (DMOS) as a switching device
App. Notes: National Semiconductor
  AN 694 (H-Bridge)
  AN 558 (Power MOSFET)

## Slide 6: Direction Control
The H-Bridge Chip has a “Direction Pin” that can be set using digital logic High/Low
controls flow through the motor in the forward or reverse configuration:

## Slide 7: Speed Control
By turning our MOSFETs (switches) ON and OFF really fast, we change the average voltage seen by the motor.
This technique is called
Pulse-Width Modulation (PWM).

## Slide 8: PWM Basics
The higher the voltage seen by the motor, the higher the speed
We’ll manipulate the PWM Duty Cycle.

## Slide 9: H-Bridge Pins
Pin 1: Bootstrap 1 (10nF cap to Pin 2)
Pin 11: Bootstrap 2 (10nF cap to Pin 10)
Pin 2: Output to Motor (M+)
Pin 3: Direction Input (From PIC)
Pin 5: PWM Input (From PIC)
Pin 6: Power Supply (Vs)
Pin 7: Ground
Pin 10: Output to Motor (M-)
Pin 4: Brake, normally grounded
Pin 8: Current Sense
Pin 9: Thermal Flag
Red pins are to be connected by the user!

## Slide 10: Locked Anti-phase PWM:
Set the PWM pin to High (100% duty)
Use PWM signal on the direction pin to control duty cycle and direction:
  50% forward / 50% reverse: no net current thru motor
  60% forward / 40% reverse: net forward current thru motor
  40% forward / 60% reverse: net reverse current thru motor

## Slide 11: Using The PIC for Motor Control
Use the PIC to generate digital logic signals to control our H-Bridge
We’ll need
  A digital high/low for direction
  output_high(PIN_A0);
  A PWM signal for speed control

## Slide 12: Setting the PWM Signal
This can be tough because we need to use a timer to set the PWM frequency.
We also need to figure out how to control the PWM duty cycle.

## Slide 13: Setting up a PWM Signal
Step 1:
Tell the PIC we want a PWM signal:
  setup_ccp1(CCP_PWM);
Step 2:
The PIC uses a timer called “Timer2” to control the PWM frequency.
We need to set this frequency:
  setup_timer_2(T2_DIV_BY_X, Y, Z);
But what are X, Y, and Z? We’ll go thru an example.

## Slide 14: Setting up a PWM Signal
Step 3:
Set the PWM Duty Cycle and hence the speed of the motor.
So, to start the motor, we could say:
  set_pwm1_duty(#); (0 < # < 1024)
To stop the motor, we could say:
  set_pwm1_duty(0);

## Slide 15: 5.0 Motor Encoders
Motor Encoders allow for us to track how far our robot has travelled.
The encoders count wheel revolutions using optical sensors.
These sensors count notches on the Drive Shaft of the motor.

## Slide 16: Some Encoder Details…
There are 512 notches on the drive shaft.
There is a 59:1 gear ratio. (This means the drive shaft spins 59x faster than the wheel.)
The top gear-down speed is around 30-60 rpm.

## Slide 17: Some Electrical Details…
The encoders we’ll be using have 4 wires:
  5V Power Supply (Red)
  GND (Black)
  Channel A a.k.a. CHA (Blue)
  Channel B a.k.a. CHB (Yellow)
Channels A&B will give us the signals to count wheel revolutions.

## Slide 18: How Encoders Work
CHA and CHB are actually square waves separated by 900.

## Slide 19: Counting Encoder Cycles
So, if we know the current encoder state and the last encoder state, we can tell which direction we’re going.
By counting the number of times we’ve changed states, we can tell how far we’ve gone.
Just remember that there are 4 encoder states per notch!

## Slide 20: RC Servo Basic
1 ms: servo is positioned at extreme left
1.5 ms: servo position at Centre
2 ms: servo is positioned at extreme right
RC servo is controlled by Pulse code Modulation at 50 Hz (20ms period):

## Slide 21: RC Servo Basic Continued
3 wires: red: (+4.5 to 6.0 V), black: ground, white: PCM Control
Can be controlled by a PIC I/O pin
Sample Analog test driver (http://www.uoguelph.ca/~antoon/gadgets/servo4.htm)

## Slide 22: Sample Program
Written in C, using CCS-C compiler
Read the IR detector output
  Approx. 0-2.5V, 10 bit resolution
Use digitized IR output to modulate a PWM signal
Use the PWM to drive an H-Bridge connected a motor
Ref: Tom Pike’s demo program

## Slide 23
// This program reads the input from the IR sensor on pin A0 and puts the
// value on the PWM ports to vary the motor speed. It also sends the value to
// the serial port.
#include<16F877.H>
#device adc=10; //Set ADC to 10 bit
#fuses HS,NOWDT,NOPROTECT,NOBROWNOUT,NOPUT //Configuration Fuses
#use delay(clock=20000000) //20Mhz Clock for wait functions
#use rs232(baud=9600,xmit=PIN_c6,rcv=PIN_C7,PARITY=N,BITS=8)//set up RS-232
#org 0x1F00,0x1FFF{} //Reserve Memory for Bootloader
long ADC_Result; //unsigned 16 bit number to hold ADC result
void main() {
puts("PIC16F877 - ADC Test\r\n"); //Print a message to serial port.
setup_adc_ports(ANALOG_RA3_REF); //all analog with Vref on pin AN3
setup_adc(ADC_CLOCK_DIV_32); //Set ADC conversion clock speed.
set_adc_channel(0); //set ADC channel to port 0 (pin 2, AN0).
setup_ccp1(CCP_PWM); //Set up PWM on CCP1.
setup_ccp2(CCP_PWM); //Set up PWM on CCP2.
setup_timer_2(T2_DIV_BY_4,254,10); //set up Timer2 for 4901Hz PWM Period …
set_pwm1_duty(0); //Start with duty cycle of 0%.
set_pwm2_duty(0); //Start with duty cycle of 0%.
output_high(pin_D1); //set direction for motor1.
output_high(pin_D2); //set direction for motor2.
while (true) {
ADC_Result = read_ADC();
set_pwm1_duty(ADC_Result); //Vary motor speed with ADC result.
set_pwm2_duty(ADC_Result); //Vary motor speed with ADC result.
printf("ADC = %4Lu\r",ADC_Result); //Send adc result to serial port.
delay_ms(200);
}
}

## Slide 24: Headers
#include<16F877.H>
// Tell Compiler that we’re using This PIC
//
#device adc=10;
//Set ADC to 10 bit
//
#fuses HS,NOWDT,NOPROTECT,NOBROWNOUT,NOPUT
//Configure Fuses:
// HS: Using High Speed Crystal/Resonator for clock
// NOWDT: No watchdog timeout
// NOPROTECT: no code protection from illegal copying
// NOBROWNOUT: no low VDD protection
// NOPUT: No Power Up Timer (72ms delay)

## Slide 25: Configuration …
#use delay(clock=20000000)
//20Mhz Clock for wait functions
//
#use rs232(baud=9600,xmit=PIN_c6,rcv=PIN_C7,PARITY=N,BITS=8)
// set up RS-232
// For communicating with HyperTerminal from the PC
//
#org 0x1F00,0x1FFF{}
// Reserve Memory for Bootloader
// For in-circuit programming
//
long ADC_Result;
// unsigned 16 bit number to hold ADC Result
//

## Slide 26: Setup ADC
void main() {
puts("PIC16F877 - ADC Test\r\n");
// Print a message to serial port.
setup_adc_ports(ANALOG_RA3_REF);
// all analog with Vref on pin RA3
// use voltage divider to put 2.5V for full scale
setup_adc(ADC_CLOCK_DIV_32);
//Set ADC conversion clock speed
// TAD (per bit) = 1/ 20MHz x 32 = 0.16 microsecond
// Requires min. 12 TAD for 10 bit
// Min. conversion time approx. 2 microsecond
set_adc_channel(0);
//set ADC channel to port 0 (pin 2, AN0).

## Slide 27: Setup PWM
setup_ccp1(CCP_PWM);
//Set up PWM output on CCP1.
setup_ccp2(CCP_PWM);
//Set up PWM output on CCP2.
setup_timer_2(T2_DIV_BY_4,254,10);
// set up Timer2 for 4921Hz PWM Period
// T2 clock speed = 20 MHz / 4 / 4, period = 0.05 x 16 = 0.8 µsec
// 254 x 0.8µsec = 0.203 msec, or 4.921 KHz
// the duty cycle will change every 0.203 msec x 10 = 2.03 msec

## Slide 28: Initialize PWM
set_pwm1_duty(0);
//Start with duty cycle of 0% on H-Bridge 1
set_pwm2_duty(0);
//Start with duty cycle of 0% on H-Bridge 2
output_high(pin_D1);
//set direction for motor1.
output_high(pin_D2);
//set direction for motor2.

## Slide 29: Main Loop
while (true) {
ADC_Result = read_ADC();
set_pwm1_duty(ADC_Result);
set_pwm2_duty(ADC_Result);
// Vary speeds of Motors 1 and 2 with ADC result.
printf("ADC = %4Lu\r",ADC_Result);
// Send ADC result to serial port.
delay_ms(200)
// do this 5 times per second
}